## Slide 1: CHAPTER 7: Finite State Machine (FSM) Principle

## Slide 2: Syllabus
Week | Content | Notes
1 | Chapter 0: Course Introduction (1) Chapter 1: Introduction to Digital Design (2) | 
2 | Chapter 2: Overview of HDL (3) | 
3 | Chapter 3: Basic Language Constructs of VHDL (3) | 
4, 5 | Chapter 4: Signal Assignment Statements of VHDL (6) | 
6 | Chapter 5: Combinational Logic Circuit Design (3) | 
7 | Midterm Exam (2) | 
8 | Chapter 6: Sequential Logic Circuit Design (3) | 
9, 10 | Chapter 7: Finite State Machine (FSM) Principle (6) | 

## Slide 3: Content
Overview of FSMs
FSMs
FSMs in VHDL
Example
ASM Charts

## Slide 4: 1. Overview of FSM
Datapath vs. Controller
Structure of a Typical Digital System
Datapath
(Execution
Unit)
Controller
(Control
Unit)
Data Inputs
Data Outputs
Control & Status Inputs
Control & Status Outputs
Control
Signals
Status
Signals

## Slide 5: 1. Overview of FSM (Datapath – Execution Unit)
Manipulate and process data
Perform arithmetic and logic operations, shifting/rotating, and other data-processing
Composed of registers, multiplexers, adders, decoders, comparators, ALUs, gates, etc.
Provides all necessary resources and interconnects among them to perform specified task.
Interprets control signals from the controller and generates status signals for controller.

## Slide 6: 1. Overview of FSM (Controller Unit)
Controls data movement in the datapath by switching multiplexers and enabling or disabling resources.
  Example: Enable signals for registers
  Example: select signals for muxes
Provides signals to active various processing tasks in the datapath, i.e., +, -, or *, …
Determine the sequence of operations performed by the datapath
Follows some ‘program’ or schedule.

## Slide 7: 1. Overview of FSM (Controller Unit)
Controller can be programmable or non-programmable
Programmable
  Has a program counter which points to next instruction
  Instructions are held in a RAM or ROM
  Microprocessor is an example of programmable controller
Non-Programmable
  Once designed, implements the same functionality
  Another term is a “hardwired state machine”, or “hardwired FSM”, or “hardwired instructions”.
  In this course, we will be focusing on non-programmable controllers.

## Slide 8: 1. Overview of FSM
Controllers can be described as Finite State Machines (FSMs)
FSMs can be represented using
  State Diagrams and State Tables – suitable for simple controllers with a relatively few inputs and outputs
  Algorithmic State Machine (ASM) Charts
All of these descriptions can be easily translated to the corresponding synthesizable VHDL code.

## Slide 9: 1. Overview of FSM (Step of Design Process)
Text description
Define interface
Describe the functionality using pseudo-code
Convert pseudo-code to FSM in state diagram
  Define states and state transitions
  Define datapath operations in each state
Develop VHDL code to implement FSM
Develop testbench for simulation and debugging
Implementation and timing simulation
  Timing simulation can reveal more bugs and pre-synthesis simulation.
Test the implement on FPGA boards

## Slide 10: 2. FSMs
An FSM is used to model a system that transits among a finite number of internal states. The transitions depend on the current state and external input.
The main application of an FSM is to act as the controller of a medium to large digital system.
Design a FSMs involves
  Define states
  Define state transitions
  Define operations performed in each state
  Optimize/minimize FSM
Manual optimization/minimization is practical for small FSMs only.

## Slide 11: 2. FSMs (Moore FSM)
Output is a function of the present state only
State register
Next State
function
Output
function
Inputs
Present State
Next State
Outputs
clock
reset

## Slide 12: 2. FSMs (Mealy FSM)
Output is a function of the present state and the inputs
Next State
function
Output
function
Inputs
Present State
Next State
Outputs
State register
clock
reset

## Slide 13: 2. FSMs (State Diagrams)
Moore Machine
State operations: output assignments depends on the state
Transition conditions: Boolean expressions
transition condition 1
transition condition 2
State 1 /
operations
State 2 /
operations

## Slide 14: 2. FSMs (State Diagrams)
Mealy Machine
State operations: datapath operations including output assignments
Transition conditions: Boolean expressions
transition condition 1 /
datapath operations
transition condition 2 /
datapath operations
State 1 /
operations
State 2 /
operations

## Slide 15: 2. FSMs (Example 1)
Moore FSM that recognizes sequence “10”
reset
Meaning
of states:
S0: No
elements
of the
sequence
observed
S1: “1”
observed
S2: “10”
observed
1
0
1
0
0
1
S0 / 0
S1 / 0
S2 / 1

## Slide 16: 2. FSMs (Example 1)
Mealy FSM that recognizes sequence “10”
S0
S1
0 / 0
1 / 0
1 / 0
0 / 1
reset
Meaning
of states:
S0: No
elements
of the
sequence
observed
S1: “1”
observed

## Slide 17: 2. FSMs (Example 1)
clock
input
Moore
Mealy
0 1 0 0 0
S0 S0 S1 S2 S0 S0
S0 S0 S1 S0 S0 S0
state
output
state
output

## Slide 18: 2. FSMs (Moore vs. Mealy FSM)
Moore and Mealy FSMs are functionally equivalent.
  Equivalent Mealy FSM can be derived from Moore FSM and vice versa
Mealy FSM has richer description and usually requires less number states
  Smaller circuit area
Mealy FSM computes output as soon as inputs change
  Mealy FSM responds one clock cycle sooner than equivalent Moore FSM
  There are direct paths from inputs to outputs, may cause glitches.
Moore FSM has no combinational path between inputs and outputs.
  Less likely to affect the critical path of the entire circuit.

## Slide 19: 2. FSMs (Moore vs. Mealy FSM)
Which way to go?
Safer.
Less likely to affect
the critical path.
Mealy FSM
Moore FSM
Lower Area
Responds one clock
cycle earlier
Fewer states

## Slide 20: 3. FSMs in VHDL
FSMs can be easily described with processes.
Synthesis tools understand FSM description if certain rules are followed.
  State transitions should be described in a process sensitive to clock and asynchronous reset signal only.
  Output function described using rules for combinational logic, i.e., as concurrent statements or a process with all inputs in the sensitivity list.

## Slide 21: 3. FSMs in VHDL (Moore FSM)
State Register
Next State
function
Output
function
Inputs
Present State
Next State
Outputs
process(clock, reset)
concurrent
statements
clock
reset

## Slide 22: 3. FSMs in VHDL (Mealy FSM)
Next State
function
Output
function
Inputs
Present State
Next State
Outputs
State Register
process(clock, reset)
concurrent
statements
clock
reset

## Slide 23: 3. FSMs in VHDL (Moore FSM – Example 1)
Moore FSM that recognizes Sequence “10”
S0 / 0
S1 / 0
S2 / 1
0
0
0
1
1
1
reset

## Slide 24: 3. FSMs in VHDL (Moore FSM – Example 1)
S0 / 0
S1 / 0
0
1
next state logic

## Slide 25: 3. FSMs in VHDL (Moore FSM – Example 1)
next state logic

## Slide 26: 3. FSMs in VHDL (Mealy FSM – Example 1)
Mealy FSM that recognizes Sequence “10”
S0
S1
0 / 0
1 / 0
1 / 0
0 / 1
reset

## Slide 27: 3. FSMs in VHDL (Mealy FSM – Example 1)
next state logic

## Slide 28: 3. FSMs in VHDL (Mealy FSM – Example 1)
next state logic

## Slide 29: 3. FSMs in VHDL
Generalized FSM

## Slide 30: 4. Example: Control Unit – Arbiter
Arbiter
reset
r1
r2
r3
g1
g2
g3
clock

## Slide 31: 4. Example: Control Unit – Arbiter

## Slide 32: 4. Example: Control Unit – Arbiter
ENTITY arbiter IS
PORT(Clock, Resetn : IN STD_LOGIC ;
r : IN STD_LOGIC_VECTOR(1 TO 3);
g : OUT STD_LOGIC_VECTOR(1 TO 3));
END arbiter;
ARCHITECTURE Behavior OF arbiter IS
TYPE State_type IS (Idle, gnt1, gnt2, gnt3);
SIGNAL state: State_type;
begin

## Slide 33: 4. Example: Control Unit – Arbiter
PROCESS(Resetn, Clock)
BEGIN
IF Resetn = '0' THEN
state <= Idle ;
ELSIF (Clock'EVENT AND Clock = '1') THEN
CASE state IS
WHEN Idle =>
IF r(1) = '1' THEN state <= gnt1 ;
ELSIF r(2) = '1' THEN state <= gnt2 ;
ELSIF r(3) = '1' THEN state <= gnt3 ;
ELSE state <= Idle ;
END IF ;
WHEN gnt1 =>
IF r(1) = '1' THEN state <= gnt1 ;
ELSE state <= Idle ;
END IF ;
-- continue on the next slide

## Slide 34: 4. Example: Control Unit – Arbiter
WHEN gnt2 =>
IF r(2) = '1' THEN state <= gnt2 ;
ELSE state <= Idle ;
END IF ;
WHEN gnt3 =>
IF r(3) = '1' THEN state <= gnt3 ;
ELSE state <= Idle ;
END IF ;
END CASE ;
END IF ;
END PROCESS ;
-- continue on the next slide

## Slide 35: 4. Example: Control Unit – Arbiter
-- output function
g(1) <= '1' WHEN y = gnt1 ELSE
'0’;
g(2) <= '1' WHEN y = gnt2 ELSE
'0’;
g(3) <= '1' WHEN y = gnt3 ELSE
'0’;
END architecture Behavior ;

## Slide 36: 4. Example: Fibonacci Number

## Slide 37: 4. Example: Fibonacci Number
idle/
rdy <=‘1’
done/
done <= ‘1’
op
i=1/
t1 <= 1
t0 <= 0
i<=n/
t1 <= t1+t0
t0 <= t1
i <= i+1
i>n
rdy: input ready
done: result is available
i: running variable
n: number of iterations
t0: holds fib(i-2)
t1: holds fib(i-1)

## Slide 38: Differences: Signals vs. Variables
Variables can only de declared and used within processes or procedures.
  Used to hold temporary results
Signals can only be declared in architecture
  Used for inter-process communications
Variables are updated immediately
Signals are updated after current execution of a process is finished
Synthesis results:
  Variables: wires or nothing
  Signals: wires, registers, or latches

## Slide 39: Differences: Signals vs. Variables
architecture sig_ex of test is
signal out1 : std_logic;
begin
process (clk)
begin
if rising_edge(clk) then
out1 <= a and b;
out2 <= out1 xor c;
end if;
end process;
end sig_ex;
FF
FF
AND
XOR
a
b
c
out1
out2

## Slide 40: Differences: Signals vs. Variables
architecture var_ex of test is
begin
process (clk)
variable out3 : std_logic;
begin
if rising_edge(clk) then
out3 := a and b;
out4 <= out3 xor c;
end if;
end process;
end var_ex;
AND
XOR
a
b
c
FF
out3
out4

## Slide 41: 5. Algorithmic State Machine (ASM)
Algorithmic State Machine: representation of a Finite State Machine suitable for FSMs with a larger number of inputs and outputs compared to FSMs expressed using state diagrams and state tables.
Output signals
or actions
(Moore type)
State name
Condition
expression
0 (False)
1 (True)
Conditional outputs
or actions (Mealy type)
(a) State box
(b) Decision box
(c) Conditional output box

## Slide 42: 5. ASM: State Box
A state box represents a state
Equivalent to a node in a state diagram or a row in a state table.
Contains register transfer actions or output signals
Moore-type outputs are listed inside of the box
It is customary to write only the name of the signal that has to be asserted in the given state, e.g., instead of <= 1.
Also, it might be useful to write an action to be taken, e.g., <= , and only later translate it to asserting control signal that causes a given action to take place (e.g., enable signal of a counter).
Output signals
or actions
(Moore type)
State name

## Slide 43: 5. ASM: Decision Box
A decision box indicates that a given condition is to be tested and the exit path is to be chosen accordingly.
The condition expression may include one or more inputs to the FSM.
Condition
expression
0 (False)
1 (True)

## Slide 44: 5. ASM: Conditional Output Box
A conditional output box denotes output signals that are of the Mealy type.
The condition that determines whether such outputs are generated is specified in the decision box.
Conditional outputs
or actions (Mealy type)

## Slide 45: 5. ASM: Moore FSM Example
ASMs can model both Mealy and Moore FSMs.
They also model machines that are of mix type.
C
z
1
=
¤
Reset
B
z
0
=
¤
A
z
0
=
¤
w
0
=
w
1
=
w
1
=
w
0
=
w
0
=
w
1
=
Moore FSM: State Diagram

## Slide 46: 5. ASM: Moore FSM Example
Moore FSM: State Table
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1

## Slide 47: 5. ASM: Moore FSM Example
Moore FSM: ASM Chart

## Slide 48: 5. ASM: Moore FSM Example
Moore FSM: VHDL Code
entity simple is
port( clock : in STD_LOGIC;
resetn : in STD_LOGIC;
w : in STD_LOGIC;
z : out STD_LOGIC);
end simple ;
architecture Behavior of simple is
type State_type IS (A, B, C) ;
signal state : State_type ;
begin
process( resetn, clock )
begin
if resetn = '0' then
state <= A ;
elsif rising_edge(Clock) then

## Slide 49: 5. ASM: Moore FSM Example
case state is
when A =>
if w = '0' then
state <= A ;
else
state <= B ;
end if;
when B =>
if w = '0' then
state <= A ;
else
state <= C ;
end if;
when C =>
if w = '0' then
state <= A ;
else
state <= C ;
end if;
end case;

## Slide 50: 5. ASM: Moore FSM Example
END IF;
END PROCESS;
z <= '1' when state = C else
'0’;
END Behavior;

## Slide 51: 5. ASM: Mealy FSM Example
Mealy FSM: State Diagram
A
w
0
=
z
0
=
¤
w
1
=
z
1
=
¤
B
w
0
=
z
0
=
¤
Reset
w
1
=
z
0
=
¤

## Slide 52: 5. ASM: Mealy FSM Example
Mealy FSM: ASM Chart
A
w
0
=
z
0
=
¤
w
1
=
z
1
=
¤
B
w
0
=
z
0
=
¤
Reset
w
1
=
z
0
=
¤

## Slide 53: 5. ASM: Mealy FSM Example
entity Mealy is
PORT ( clock : IN STD_LOGIC;
resetn : IN STD_LOGIC;
w : IN STD_LOGIC;
z : OUT STD_LOGIC);
end Mealy;
architecture Behavior of Mealy is
type State_type is (A, B) ;
signal state: State_type ;
begin
process (resetn, clock)
begin
if resetn = '0' then
state<= A ;
elsif rising_edge(clock) then

## Slide 54: 5. ASM: Mealy FSM Example
A
w
0
=
z
0
=
¤
w
1
=
z
1
=
¤
B
w
0
=
z
0
=
¤
Reset
w
1
=
z
0
=
¤

## Slide 55: 5. ASM: Mealy FSM Example
z <= '1' when (y = B) and (w=‘1’) else
'0’;
end architecture Behavior ;
A
w
0
=
z
0
=
¤
w
1
=
z
1
=
¤
B
w
0
=
z
0
=
¤
Reset
w
1
=
z
0
=
¤

## Slide 56: 5. ASM: Summary
ASM Chart
Flowchart-like diagram
Provides the same information as a state diagram
More descriptive, better for complex description
ASM block
  One state block
  One or more optional decision boxes:
  with T (1) or F (0) exit path
  One or more conditional output boxes:
  for Mealy output

## Slide 57: 5. ASM: Summary

## Slide 58: 5. ASM: Chart Rules
Difference between a regular flowchart and an ASM chart
  Transition governed by clock
  Transition occurs between ASM blocks
Basic rules:
  For a given input combination, there is one unique exit path from the current ASM block
  Any closed loop in an ASM chart must include a state box.

## Slide 59: 5. ASM: Incorrect ASM Chart

## Slide 60: 5. ASM: Incorrect ASM Chart

## Slide 61: 5. ASM: Example
Design a circuit that counts the number of bits set to 1 in an n-bit input A ().
Is any problem with this design?
S1 is the initial state, result = 0 and data is loaded into a register A until a start signal s, is asserted.
The ASM chart then transitions to state S2, where it increments the result to count the number of 1’s in register A.
When register A is equal to 0 the ASM chart transitions to state S3, where it sets an output Done = 1 and waits for the signal s to be deasserted

## Slide 62: 5. ASM: Example
Design a circuit that produces the 2n-bit product of two n-bit numbers placed on the Multiplier and Multiplicand inputs
Multiplication is initiated by the first clock pulse that occurs after the “Go” input is set HI
If the output IDLE= 1, the circuit is not busy, i.e. ready to multiply
While a multiply operation is taking place, IDLE = 0
These two signals (IDLE and Go) may be used to coordinate the timing of the binary multiplier with the external user. This is known as “handshaking”.
The Reset input is used to force the circuit (asynchronously) to the IDLE state at any time (such as at power-up)